## Slide 1: 実装課題
事象が三つ、それ以上か
  ①ERROR_COUNTに+が設定される
    原因①ジョブコントロール変数が文字型
      IFアイコンを文字型で判定したがだめ
    原因②ジョブコントロール変数が未定義
      変数アイコンで定義したがだめ
    原因③ジョブアイコンで削除してる
      ジョブアイコンで定義したがだめ
    原因④並行処理で変数が削除される
      変数をジョブごとに定義
      実行時間をずらす
  ②exprのexit_code=64512になる
    計算アイコンを使用せず、IFアイコンをつなげるジョブネットに変更して回避(可読性が悪い)
  ③can not find inner_job_id: 139983 or value_name
    これもダメ
本番への影響
  サーバー障害にならない限りエラーは発生しないと想定される? (本当か?)

## Slide 2: 製品仕様
Windows Agent並行処理でエラーが発生
  製品仕様の原因
    「WindowsAgentのジョブ実行プロセスでは、同一サーバ内はSingleObjectでの起動」
    回避策は「エージェントレス」アイコンは並行の制限なし
  関連情報
      Job Arranger for Zabbixの設定方法について
        https://www.jobarranger.info/redmine/issues/2888
      処理終了後もmanager「ジョブ実行管理」のステータスが実行中のままになる件
        https://www.jobarranger.info/redmine/issues/2920
  関連するリリースノート
    2017-09-19 : Version 3.4.0
      Windowsエージェントで多数ジョブ同時実行の過負荷時に起きうるエラー解消
        SQLiteのjournalファイルを掴みあった際にPermission deniedエラーが起きる問題解消
        プロセス終了後にも一時ファイルが残り、プロセス無エラーとなる問題解消
      変数アイコンで異例な変数値セットの失敗時にはエラー停止
    2014-07-16 : Version 2.0.1
      ジョブネットの多重起動抑止機能を追加

## Slide 3: 実装課題
環境変数
  ローカル変数(ジョブアイコン内のみで参照可能)
    ジョブ変数 ⇒ジョブアイコン内でのみ環境変数として使用可能
  グローバル変数(ジョブネット間で参照可能)
    ジョブコントローラ変数 ⇒ジョブネット内の全アイコンで環境変数として利用可能
    ジョブ停止コード(Job stop code) ⇒0～10の32乗、(カンマかハイフンで指定可能)
    アイコン状態(ICON_STATUS) ⇒0:正常終了、1:停止コード検出、2:処理エラー
    ジョブの戻り値(JOB_EXIT_CD) ⇒0～255

## Slide 4: 実装課題
ジョブアインの設定
  異常ジョブの復旧方法
    手動で復旧する場合
      Job stop code に範囲を指定
      Continue をオフ
    後続ジョブで復旧する場合
      Job stop code に範囲を指定
      Continue をオン
    エラーを無視する場合
      Job stop code を設定しない
ジョブが異常終了したときに
コマンドを指定可能
※プロジェクトでは未使用
ジョブが異常終了した際、
後続処理を実行したいときにチェック
※チェックしないと手動で処置が必要
ジョブが異常終了した際、
終了コードが自動的に設定される
※OSやAPに依存するため
事前に設定値がわからない
※自動的にジョブ制御変数が生成されるので
JOB_EXIT_CDにチェックは不要
JOB_EXIT_CDの値がJob stop codeの
範囲内の場合、ジョブの異常終了とみなす
※ICON_STATUSに下記のいずれかが設定される
1: 停止コード検出
2: 処理エラー
ジョブの実行結果はJOB_EXIT_CDに格納されるが、
複数のコマンドを実行した場合、最後のコマンドの
実行結果がJOB_EXIT_CDに格納される
※複数のコマンドを実行する際は異常終了を
判断するため専用のジョブ変数などの定義が必要
ジョブ変数はジョブアイコン内でのみ
環境変更として参照可能(更新不可)
※コマンド引数の引き渡しに使えるが、
プロジェクトでは未使用
ジョブ制御変数はジョブネット内で
環境変数として使用可能
子ジョブネットに引き継げるが、
親ジョブネットに引き継げない

## Slide 5: 実装課題
変数アイコン(Variable)
  ジョブの異常を検知するため、ジョブネットの最初にJOB_EXIT_CD = 0を設定
    ジョブネット実行時にJOB_EXIT_CDジョブネット変数は生成されず、最初のジョブが異常終了すると後続の計算アイコン(Calc)で計算できず異常終了することを防ぐ
  ERROR_COUNTが0を超えたら異常と判断する
    ERROR_COUNT = ERROR_COUNT + ICON_STATUS + JOB_EXIT_CD

## Slide 6: 実装課題
IFアイコンで異常終了する判定
  ERROR_COUNT+ ICON_STATUS+JOB_EXIT_CD = 0
    ICON_STATUS (Host nameが起動中か)
    JOB_EXIT_CD (コマンド実行が正常か)
  ERROR_COUNT > 0で異常終了に分岐
最初にジョブネット
変数を定義する
JOB_EXIT_CD = 0
サーバー停止の場合
ICON_STATUS = 2
コマンド異常終了
ICON_STATUS = 1
JOB_EXIT_CD = 不定
IFアイコンで判断するため「Continue」オン
Job stop codeを省略すると
異常と判断されないため設定

## Slide 7: 実装課題
検出できないエラー
  存在しないドライブレターを指定するとエラーを検知できない
    Cドライブ、Dドライブ構成のサーバーの場合、 Dドライブにコマンドファイルを配置し、 誤ってEドライブと指定した場合、エラーを検知できない
      ただし、Cドライブは存在するのでエラーを検知可能
正しくはDドライブ
仮にEドライブと指定
異常終了せずに
処理が継続する
Eドライブの場合、標準エラー出力に表示されるが
ICON_STATUSとJOB_EXIT_CDは正常
Cドライブはエラーを検知

## Slide 8: 実装課題
テスト実行で計算アイコンの結果不正
  再現性なし、エラーを伴う並行処理の影響が懸念される
    並行処理で分岐すると、異なる変数として識別される
ERROR_COUNTに”+”
が設定された原因不明
テスト実行の問題なのか判断できないため、
並行処理で変数を使う際は注意が必要

## Slide 9: 実装課題
テスト実行の再現性
実行中で終了しない
ERROR_COUNTに”+”
が設定された原因不明

## Slide 10: 実装課題
サブジョブネット(子)でジョブが異常終了してもアイコンが赤くならない
JN0353000のコマンドジョブが異常終了したので
ジョブネットが赤く表示されてほしいが、
緑のままなので視覚的に異常を検知できない
※この処理は後続JN0367000でリトライするので
処理は正常に終了するので問題なし

## Slide 11: 実装課題
計算アイコンの結果不正
  変数を初期化しないと+が設定される?

## Slide 12: 実装課題
計算アイコンで原因不明のエラー発生

## Slide 13: 実装課題
JOB=JN0512000/JB0513000
  16938:20200129:113738.698 [ERROR] In message_send() failed to execute the command. command: (2) [/usr/bin/zabbix_sender -z '192.168.100.28' -p '10051' -s 'Zabbix server' -k 'jasender' -o '[2020/01/29 11:37:37] [ERROR] [JARUNICONJOB200012] Cannot send data:inner_jobid [117405], message [hostname 'ERINGITEN_taskkicker' does not match Hostname] (USER NAME=Admin HOST=ERINGITEN_taskkicker JOBNET=JN0512000 JOB=JN0512000/JB0513000 INNER_JOBNET_MAIN_ID=1500000000000000773)']
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000102"
  sent: 1; skipped: 0; total: 1
  16938:20200129:113738.864 [ERROR] In message_send() failed to execute the command. command: (2) [/usr/bin/zabbix_sender -z '192.168.100.28' -p '10051' -s 'Zabbix server' -k 'jasender' -o '[2020/01/29 11:37:38] [INFO] [JAJOBNETRUN000001] In ja_set_runerr() job execution error. inner_job_id: 117405 status is RUNERR jobnet_id: JN0512000, job_id: JN0512000/JB0513000, user_name: Admin, job_exit_cd: 0, icon_status: 2 (USER NAME=Admin HOST=ERINGITEN_taskkicker JOBNET=JN0512000 JOB=JN0512000/JB0513000 INNER_JOBNET_MAIN_ID=1500000000000000773)’]
JOB=JN0512000/CAL-1
  expr: syntax error
  15132:20200129:113738.927 [ERROR] [JARUNICONCALC200004] In jarun_icon_calc() can not get value. command: expr $ICON_STATUS \+ $JOB_EXIT_CD
  16929:20200129:113738.933 [ERROR] [JARUNICONCALC200005] In jarun_icon_calc() exit_code: 64512
  16929:20200129:113738.945 [INFO] [JAJOBNETRUN000001] In ja_set_runerr() job execution error. inner_job_id: 117364 status is RUNERR jobnet_id: JN0512000, job_id: JN0512000/CAL-1, user_name: Admin, job_exit_cd: , icon_status:
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000100"
  sent: 1; skipped: 0; total: 1
  16938:20200129:113740.128 [ERROR] In message_send() failed to execute the command. command: (2) [/usr/bin/zabbix_sender -z '192.168.100.28' -p '10051' -s 'Zabbix server' -k 'jasender' -o '[2020/01/29 11:37:38] [ERROR] [JARUNICONCALC200004] In jarun_icon_calc() can not get value. command: expr $ICON_STATUS \+ $JOB_EXIT_CD (USER NAME=Admin HOST=JAZServer JOBNET=JN0512000 JOB=JN0512000/CAL-1 INNER_JOBNET_MAIN_ID=1500000000000000773)']
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000082"
  sent: 1; skipped: 0; total: 1
  16938:20200129:113740.198 [ERROR] In message_send() failed to execute the command. command: (2) [/usr/bin/zabbix_sender -z '192.168.100.28' -p '10051' -s 'Zabbix server' -k 'jasender' -o '[2020/01/29 11:37:38] [ERROR] [JARUNICONCALC200005] In jarun_icon_calc() exit_code: 64512 (USER NAME=Admin HOST=JAZServer JOBNET=JN0512000 JOB=JN0512000/CAL-1 INNER_JOBNET_MAIN_ID=1500000000000000773)']
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000142"
  sent: 1; skipped: 0; total: 1
  16938:20200129:113740.273 [ERROR] In message_send() failed to execute the command. command: (2) [/usr/bin/zabbix_sender -z '192.168.100.28' -p '10051' -s 'Zabbix server' -k 'jasender' -o '[2020/01/29 11:37:38] [INFO] [JAJOBNETRUN000001] In ja_set_runerr() job execution error. inner_job_id: 117364 status is RUNERR jobnet_id: JN0512000, job_id: JN0512000/CAL-1, user_name: Admin, job_exit_cd: , icon_status: (USER NAME=Admin HOST=JAZServer JOBNET=JN0512000 JOB=JN0512000/CAL-1 INNER_JOBNET_MAIN_ID=1500000000000000773)']

## Slide 14: 実装課題
計算アイコンで原因不明のエラー発生

## Slide 15: 実装課題
同時刻に実行するジョブネットとジョブコントロール変数が重複しているのが原因と考えられないか
JN1318000/JB1318100
  9222:20200129:182001.588 [ERROR] [JARUNICONJOB200012] Cannot send data:inner_jobid [126203], message [hostname 'IRPPWBSVA01' does not match Hostname]
  9222:20200129:182001.819 [INFO] [JAJOBNETRUN000001] In ja_set_runerr() job execution error. inner_job_id: 126203 status is RUNERR jobnet_id: JN1318000, job_id: JN1318000/JB1318100, user_name: Admin, job_exit_cd: 0, icon_status: 2
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000138"
  sent: 1; skipped: 0; total: 1
JN1318000/CAL-1
  expr: syntax error
  9281:20200129:182002.004 [ERROR] [JARUNICONCALC200004] In jarun_icon_calc() can not get value. command: expr $ICON_STATUS \+ $JOB_EXIT_CD
  4144:20200129:182002.015 [ERROR] [JARUNICONCALC200005] In jarun_icon_calc() exit_code: 64512
  4144:20200129:182002.021 [INFO] [JAJOBNETRUN000001] In ja_set_runerr() job execution error. inner_job_id: 126198 status is RUNERR jobnet_id: JN1318000, job_id: JN1318000/CAL-1, user_name: Admin, job_exit_cd: , icon_status:
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000137"
  sent: 1; skipped: 0; total: 1
  4153:20200129:182002.032 [ERROR] In message_send() failed to execute the command. command: (2) [/usr/bin/zabbix_sender -z '192.168.100.28' -p '10051' -s 'Zabbix server' -k 'jasender' -o '[2020/01/29 18:20:01] [ERROR] [JARUNICONJOB200012] Cannot send data:inner_jobid [126203], message [hostname 'IRPPWBSVA01' does not match Hostname] (USER NAME=Admin HOST=IRPPWBSVA01 JOBNET=JN1318000 JOB=JN1318000/JB1318100 INNER_JOBNET_MAIN_ID=4881)']
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000135"
  sent: 1; skipped: 0; total: 1
  4153:20200129:182002.339 [ERROR] In message_send() failed to execute the command. command: (2) [/usr/bin/zabbix_sender -z '192.168.100.28' -p '10051' -s 'Zabbix server' -k 'jasender' -o '[2020/01/29 18:20:01] [INFO] [JAJOBNETRUN000001] In ja_set_runerr() job execution error. inner_job_id: 126203 status is RUNERR jobnet_id: JN1318000, job_id: JN1318000/JB1318100, user_name: Admin, job_exit_cd: 0, icon_status: 2 (USER NAME=Admin HOST=IRPPWBSVA01 JOBNET=JN1318000 JOB=JN1318000/JB1318100 INNER_JOBNET_MAIN_ID=4881)']
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000147"
  sent: 1; skipped: 0; total: 1
  4153:20200129:182003.486 [ERROR] In message_send() failed to execute the command. command: (2) [/usr/bin/zabbix_sender -z '192.168.100.28' -p '10051' -s 'Zabbix server' -k 'jasender' -o '[2020/01/29 18:20:02] [ERROR] [JARUNICONCALC200004] In jarun_icon_calc() can not get value. command: expr $ICON_STATUS \+ $JOB_EXIT_CD (USER NAME=Admin HOST=JAZServer JOBNET=JN1318000 JOB=JN1318000/CAL-1 INNER_JOBNET_MAIN_ID=4881)']
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000083"
  sent: 1; skipped: 0; total: 1
  4153:20200129:182003.555 [ERROR] In message_send() failed to execute the command. command: (2) [/usr/bin/zabbix_sender -z '192.168.100.28' -p '10051' -s 'Zabbix server' -k 'jasender' -o '[2020/01/29 18:20:02] [ERROR] [JARUNICONCALC200005] In jarun_icon_calc() exit_code: 64512 (USER NAME=Admin HOST=JAZServer JOBNET=JN1318000 JOB=JN1318000/CAL-1 INNER_JOBNET_MAIN_ID=4881)']
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000087"
  sent: 1; skipped: 0; total: 1

## Slide 16: 実装課題
回避策を実装したが、並行処理で64512が発生

## Slide 17: 実装課題
  expr: syntax error
  7073:20200129:205002.733 [ERROR] [JARUNICONCALC200004] In jarun_icon_calc() can not get value. command: expr $ICON_STATUS \+ $JOB_EXIT_CD
  4144:20200129:205002.782 [ERROR] [JARUNICONCALC200005] In jarun_icon_calc() exit_code: 64512
  4144:20200129:205002.811 [INFO] [JAJOBNETRUN000001] In ja_set_runerr() job execution error. inner_job_id: 126688 status is RUNERR jobnet_id: JN1318000, job_id: JN1318000/CAL-1, user_name: Admin, job_exit_cd: , icon_status:
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000120"
  sent: 1; skipped: 0; total: 1
  4153:20200129:205003.001 [ERROR] In message_send() failed to execute the command. command: (2) [/usr/bin/zabbix_sender -z '192.168.100.28' -p '10051' -s 'Zabbix server' -k 'jasender' -o '[2020/01/29 20:50:02] [ERROR] [JARUNICONJOB200012] Cannot send data:inner_jobid [126693], message [hostname 'IRPPWBSVA01' does not match Hostname] (USER NAME=Admin HOST=IRPPWBSVA01 JOBNET=JN1318000 JOB=JN1318000/JB1318100 INNER_JOBNET_MAIN_ID=4945)']
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000106"
  sent: 1; skipped: 0; total: 1
  7114:20200129:205003.174 [INFO] [JAJOBNETRUN000001] In ja_set_runerr() job execution error. inner_job_id: 126699 status is RUNERR jobnet_id: JN1318200, job_id: JN1318200/JB1318400, user_name: Admin, job_exit_cd: , icon_status: 2
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000098"
  sent: 1; skipped: 0; total: 1
  4153:20200129:205003.432 [ERROR] In message_send() failed to execute the command. command: (2) [/usr/bin/zabbix_sender -z '192.168.100.28' -p '10051' -s 'Zabbix server' -k 'jasender' -o '[2020/01/29 20:50:02] [INFO] [JAJOBNETRUN000001] In ja_set_runerr() job execution error. inner_job_id: 126693 status is RUNERR jobnet_id: JN1318000, job_id: JN1318000/JB1318100, user_name: Admin, job_exit_cd: 0, icon_status: 2 (USER NAME=Admin HOST=IRPPWBSVA01 JOBNET=JN1318000 JOB=JN1318000/JB1318100 INNER_JOBNET_MAIN_ID=4945)']
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000096"
  sent: 1; skipped: 0; total: 1
  4153:20200129:205003.609 [ERROR] In message_send() failed to execute the command. command: (2) [/usr/bin/zabbix_sender -z '192.168.100.28' -p '10051' -s 'Zabbix server' -k 'jasender' -o '[2020/01/29 20:50:02] [ERROR] [JARUNICONCALC200004] In jarun_icon_calc() can not get value. command: expr $ICON_STATUS \+ $JOB_EXIT_CD (USER NAME=Admin HOST=JAZServer JOBNET=JN1318000 JOB=JN1318000/CAL-1 INNER_JOBNET_MAIN_ID=4945)']
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000096"
  sent: 1; skipped: 0; total: 1
  4153:20200129:205003.667 [ERROR] In message_send() failed to execute the command. command: (2) [/usr/bin/zabbix_sender -z '192.168.100.28' -p '10051' -s 'Zabbix server' -k 'jasender' -o '[2020/01/29 20:50:02] [ERROR] [JARUNICONCALC200005] In jarun_icon_calc() exit_code: 64512 (USER NAME=Admin HOST=JAZServer JOBNET=JN1318000 JOB=JN1318000/CAL-1 INNER_JOBNET_MAIN_ID=4945)']
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000085"
  sent: 1; skipped: 0; total: 1
  4153:20200129:205003.725 [ERROR] In message_send() failed to execute the command. command: (2) [/usr/bin/zabbix_sender -z '192.168.100.28' -p '10051' -s 'Zabbix server' -k 'jasender' -o '[2020/01/29 20:50:02] [INFO] [JAJOBNETRUN000001] In ja_set_runerr() job execution error. inner_job_id: 126688 status is RUNERR jobnet_id: JN1318000, job_id: JN1318000/CAL-1, user_name: Admin, job_exit_cd: , icon_status: (USER NAME=Admin HOST=JAZServer JOBNET=JN1318000 JOB=JN1318000/CAL-1 INNER_JOBNET_MAIN_ID=4945)']
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000089"
  sent: 1; skipped: 0; total: 1
  7279:20200129:205101.433 [ERROR] [JARUNICONJOB200012] Cannot send data:inner_jobid [126865], message [hostname 'IRPPWBSVA01' does not match Hostname]
  7279:20200129:205101.568 [INFO] [JAJOBNETRUN000001] In ja_set_runerr() job execution error. inner_job_id: 126865 status is RUNERR jobnet_id: JN1318000, job_id: JN1318000/JB1318100, user_name: Admin, job_exit_cd: 0, icon_status: 2
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000128"
  sent: 1; skipped: 0; total: 1

## Slide 18: 実装課題
IFアイコンでもエラー発生
  Can not find value_name
    並行処理(3多重)で発生しやすい
    ICON_STATUS, JOB_EXIT_CDはチェックON

## Slide 19: 実装課題
JN1324400/JB1324500
  4322:20200130:173602.521 [ERROR] [JARUNICONJOB200012] Cannot send data:inner_jobid [139985], message [hostname 'JPINFOPSV01' does not match Hostname]
  4322:20200130:173602.768 [INFO] [JAJOBNETRUN000001] In ja_set_runerr() job execution error. inner_job_id: 139985 status is RUNERR jobnet_id: JN1324400, job_id: JN1324400/JB1324500, user_name: Admin, job_exit_cd: , icon_status: 2
  919:20200130:173602.895 [ERROR] [JARUNICONIF200003] In jarun_icon_if() can not find inner_job_id: 139983 or value_name
  919:20200130:173602.902 [INFO] [JAJOBNETRUN000001] In ja_set_runerr() job execution error. inner_job_id: 139983 status is RUNERR jobnet_id: JN1324400, job_id: JN1324400/IF-1, user_name: Admin, job_exit_cd: , icon_status:
  928:20200130:173603.088 [ERROR] In message_send() failed to execute the command. command: (2) [/usr/bin/zabbix_sender -z '192.168.100.28' -p '10051' -s 'Zabbix server' -k 'jasender' -o '[2020/01/30 17:36:02] [ERROR] [JARUNICONJOB200012] Cannot send data:inner_jobid [139985], message [hostname 'JPINFOPSV01' does not match Hostname] (USER NAME=Admin HOST=JPINFOPSV01 JOBNET=JN1324400 JOB=JN1324400/JB1324500 INNER_JOBNET_MAIN_ID=6215)']
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000027"
  sent: 1; skipped: 0; total: 1
  928:20200130:173603.220 [ERROR] In message_send() failed to execute the command. command: (2) [/usr/bin/zabbix_sender -z '192.168.100.28' -p '10051' -s 'Zabbix server' -k 'jasender' -o '[2020/01/30 17:36:02] [INFO] [JAJOBNETRUN000001] In ja_set_runerr() job execution error. inner_job_id: 139985 status is RUNERR jobnet_id: JN1324400, job_id: JN1324400/JB1324500, user_name: Admin, job_exit_cd: , icon_status: 2 (USER NAME=Admin HOST=JPINFOPSV01 JOBNET=JN1324400 JOB=JN1324400/JB1324500 INNER_JOBNET_MAIN_ID=6215)']
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000020"
  sent: 1; skipped: 0; total: 1
JN1324400/IF-1
  928:20200130:173603.267 [ERROR] In message_send() failed to execute the command. command: (2) [/usr/bin/zabbix_sender -z '192.168.100.28' -p '10051' -s 'Zabbix server' -k 'jasender' -o '[2020/01/30 17:36:02] [ERROR] [JARUNICONIF200003] In jarun_icon_if() can not find inner_job_id: 139983 or value_name (USER NAME=Admin HOST=JAZServer JOBNET=JN1324400 JOB=JN1324400/IF-1 INNER_JOBNET_MAIN_ID=6215)']
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000026"
  sent: 1; skipped: 0; total: 1
  928:20200130:173603.330 [ERROR] In message_send() failed to execute the command. command: (2) [/usr/bin/zabbix_sender -z '192.168.100.28' -p '10051' -s 'Zabbix server' -k 'jasender' -o '[2020/01/30 17:36:02] [INFO] [JAJOBNETRUN000001] In ja_set_runerr() job execution error. inner_job_id: 139983 status is RUNERR jobnet_id: JN1324400, job_id: JN1324400/IF-1, user_name: Admin, job_exit_cd: , icon_status: (USER NAME=Admin HOST=JAZServer JOBNET=JN1324400 JOB=JN1324400/IF-1 INNER_JOBNET_MAIN_ID=6215)']
  info from server: "processed: 0; failed: 1; total: 1; seconds spent: 0.000022"
  sent: 1; skipped: 0; total: 1